## Slide 1: Cresta Cooler Its time to be a ruler, install the Cresta Cooler

## Slide 2: The Problem

## Slide 3: The Problem
Indian villages face large gap between electricity demand and supply.
Only 1,417 (7.3%) of the 18,452 villages have 100% electrical connectivity; 31 million homes still without electricity.
Temperatures are nearing 500 c in some parts of the nation.
There is a need for a cost effective cooling mechanism that can be used even in the absence of electricity supply.
The Cresta Cooler is a perfect solution to this problem

## Slide 4
About the Product
“Cresta Cooler”
Cooler made from recycled and easily available materials.
Provides cooling comfort in hot areas with no or minimal electricity supply
Low cost to own and use

## Slide 5: Waste Materials Used
The Cresta Cooler is essentially a cooler that is made up of waste materials that include:
  Plastic oil box (50 litre)
  Ice-cream sticks, Twigs, broom fibers, jute
  Cardboard
1
2
3

## Slide 6
Cooler box
Switch
For Pump
DC Water Pump
Fan connected to DC motor
Water distribution tube
Thick cardboard support
Switch
For Motor
Cresta Cooler overview
Front View
Rear View
Cooler pad

## Slide 7: DETAILS OF THE PRODUCT

## Slide 8: The Body of the Cooler
Body: 4-sided 50 litre oil box
Front side: Circular opening + Plastic fan blades
Rear side: Rectangular opening + Cooler Pad
Oil Box body
Front Side
Rear Side

## Slide 9: Cooler Padding
The frame is made using ice-cream sticks and twigs filled with broom fiber/ jute
Broom fiber
Frame for Cooler Pad
Rear View
Jute fiber

## Slide 10: The Fan
The fan is attached to the DC motor and fixed inside the circular opening
Cardboard support
Front View
DC Motor
Fan Blades

## Slide 11: Functioning of The Cooler
Top of the box sealed with cardboard
Water distribution tube connected from top of box to pump
Submersible DC water pump placed inside the cooler body.
DC Water Pump and DC Fan Motor connected by wires to separate switches mounted on cooler body.
Power source is 12 V battery.
Wiring of the cooler
12 V battery
Wire from Motor
Wire from Pump
Wires from Switch

## Slide 12: How it provides Cooling?
Water is added from the front or rear side.
Pump circulates water to reduce temperatures
If there is electricity an adaptor can be used in place of a battery .
Switching mode adaptor
DC water Pump
Water added from front

## Slide 13: Battery Recharging
For the villages without any electricity we plan to set up a charging station which will comprise of 12V battery chargers with a 12V solar panel being the power source
12 V Solar panel( Power Source)
Battery charger
Recharged Battery

## Slide 14: Recharging Booth

## Slide 15: Conversion of Waste
1. A plastic oil box is reused as the body of the cooler
2.Ice- cream sticks and twigs are used to make the frame of the cooler pad
3.Broom fiber/ Jute is used to fill the pad
4.Waste cardboard is used for the support of the fan structure and to seal the top part of the cooler body

## Slide 16: Pricing (Per Unit)
COMPANY | ITEM | COST ( in ₹)
Waste Material | Cooler padding | -
Waste Material | Plastic Oil Box and Cardboard | -
Human Resource | Labour charges | 10
MX | Wires and screws | 5
Coolio | Blades | 10
GKR Plastic | Fan Blade | 15
KitsGuru | DC Water Pump (Submersible) | 60
Generic | DC Motor | 80
Generic | 12 V Battery (Rechargeable) | 50
Legal fee | Patent | 50
TOTAL |  | 280

## Slide 17: Financials
 | Year 1 (2018-2019) | Year 2 (2019-2020) | Year 3 (2020-2021 )
Revenue (Total Sales) | 75,00,000 | 1,50,00,000 | 2,25,00,000
Operating Expenses | 3,50,000 | 7,00,000 | 10,50,000
Salaries | 30,00,000 | 60,00,000 | 90,00,000
Marketing (Ads) | 20,00,000 | 30,00,000 | 40,00,000
Production Unit - Rent | 10,00,000 | 20,00,000 | 30,00,000
Legal fees (Patents) | 50,000 | 75,000 | 1,00,000
Motor (DC water pump + DC motor) | 7,00,000 | 14,00,000 | 21,00,000
Wires, Screws, Blades, Battery | 3,25,000 | 6,50,000 | 9,75,000
Charging Booth (Set-up) | 6,00,000 | 12,00,000 | 18,00,000
Total Expenses | 78,75,000 | 1,50,25,000 | 2,20,25,000
 | (-3,75,000) | (-25,000) | 4,75,000

## Slide 18: Marketing Strategies
Considering the fact that our target consumers primarily include the rural poor, we plan to:
Distribute pamphlets in 10 villages particularly in Uttar Pradesh, Punjab and Bihar.
Publish advertisements in local newspapers and radio.
Launch advertisements under the label of Ministry of Rural Development, India under the “ Pradhan Mantri Sahaj Bijli Har Ghar Yojana”
Launch an online marketing campaign and a PR campaign.

## Slide 19: Impact on Environment

## Slide 20: Competitors
Cost- ₹4500
Cost- ₹4199
Cost- ₹6950
Bajaj Coolers
Crompton Coolers
Bajaj
Ken Star Cooler

## Slide 21: Welfare of people

## Slide 22
It is time to join Team Cresta
Thank You